## Slide 1: Systems Engineering for Medical Devices
Training Material

## Slide 2: Business Strategy
A proper business strategy is a fundamental anchor for product design and development.
To define a business strategy with “strategic positioning” [1]:
    Create a unique and valuable position: serve few needs of many customers serve broad needs of few customers serve broad needs of many customers in a narrow market
    Chose what not to do.
    Create “fit” among the company’s activities. Create competitive advantage and sustainability: align activities with the strategy until they mutually reinforce each other.
  [1] Porter, M.E., 2011. Chapter 1: What is Strategy? HBR's 10 Must Reads on Strategy. Harvard Business Press

## Slide 3: Business Strategy
For a product, projects and early startups first need to find a business model.
To validate a business model, time and cost are typically limited.
Fill relevant fields of the Business Model Canvas, then validate and iterate it, ideally through early market exposure:
Key partners _ | Key activities _ | Value proposition _ |  | Customer relationships _ | Customer segments _
 | Key resources _ |  |  | Channels _ | 
Cost structure _ |  |  | Revenue streams _ |  | 
[Osterwalder, 2004. The business model ontology a proposition in a design science approach.]

## Slide 4: Business Strategy
The “Lean” variant is an alternative to the Business Model Canvas
Problem List your customer’s top 3 problems Existing alternatives List how these problems are solved today | Solution Outline a possible solution for each problem | Unique value proposition Single, clear, compelling message that turns an unaware visitor into an interested prospect High level concept List your X for Y analogy (e.g. YouTube = Flickr for videos) |  | Unfair advantage Something that can not be easily copied or bought | Customer segments List your target customers and users Early adopters List the characteristics of your ideal customers
 | Key metrics List the key numbers that tell you how your business is doing |  |  | Channels List your path to customers | 
Cost structure List your fixed and variable costs |  |  | Revenue streams List your sources of revenue |  | 
[Maurya, A., 2022. Running lean. " O'Reilly Media, Inc.”]

## Slide 5: Business Strategy
While validating a product idea, engaging in heavily regulated product development per industry standards is not suitable.
  During exploratory product development, requirements need to be identified through iterations, ideally with market exposure
  Methods, e.g.: website/shop with specifications, pre-orders/ “notify me when this product is available”, mock-ups, prototype demonstrations, expert panels
For this purpose, it may be advisable to run an agile approach before starting the regulated development.
Concept:
  Agile development (create a prototype)
    Vision-driven
    Fixed: time and cost, Flexible: deliverables (requirements)
  Get funding and structure
  Regulated product development (market release)
    Plan-driven
    Fixed: deliverables (requirements), Estimated: time and cost
    deliverables (requirements)
    cost
    time

## Slide 6: Go-To-Market Strategy
Go-to-market approach by Alpha Innomed:
  Define what constitutes the most ready and most suitable target market
  Think globally and find a favorable market (the “beach head”) among regulated and non-regulated markets
  Identify adoption barriers to reach the required market readiness

## Slide 7: Regulatory Strategy
Once the target market has been identified, identify the applicable local regulations.
Choose a regulatory pathway:
  Medical devices
    FDA: Premarket Notification 510(k), Premarket Approval (PMA), Humanitarian Device Exemption (HDE)
    Other markets: MDR (EU), NMPA (PRC), MFDS/KFDA (KOR), ANVISA (BRA) ..
  Non-medical devices
    Further reading: https://openregulatory.com/is-our-software-medical-device/
    Health and wellness applications
    Educational purpose
    Devices ”intended to be used for research applications only”/ “not designed or intended to be used for diagnosis or treatment of disease”
    Machines (EU: Machinery Directive 2006/42/EC), radio equipment (EU: Directive 2014/53/EU)

## Slide 8: Regulatory Strategy
Non-medical devices: Example for health and wellness application
  Huawei Scale 3 Pro “Compliance with the essential requirements and other relevant provisions of Directive 2014/53/EU (radio equipment directive, RAD).”
    Intended use:
      Weight measurements, body fat measurements, heart rate measurements, for use with HUAWEI Health App
      This product is not designed to be a medical device, and is not intended to diagnose, treat, cure or prevent any disease. All data and measurements should be used for personal reference only.
      The product is suitable for daily use, especially for people who would like to understand more about their weight, body shape, body fat, and musclemass. The data it provides is for personal reference only, and is not intended for medical treatment or as a basis for medical diagnosis, and should not be used in clinics or other medical institutions such as hospitals.”
  HUAWEI Health App
    Intended use:
      “The Huawei Health app is designed for fitness and wellness only. It is not intended for the diagnosis or treatment of disease or other health problems, nor for the cure or prevention of disease. Huawei makes no representations or warranties to you in this respect.”

## Slide 9: Regulatory Strategy
EU, medical devices with hardware: all active devices need to comply with EMC and EMF (these require tests in official test labs).
For any Wifi device that is put on the market, compliance with the Radio Equipment Directive (RED) needs to be demonstrated.
  Even if radio modules are installed that already comply with RED, the RED conformity must be demonstrated again for the entire device in most cases. You can avoid certain tests, but the radio module must be appropriately installed and exemptions must be substantiated by a risk analysis.
  Interesting note: How does the RPI get CE marking, even though it has an open PCB board? Answer is: it meets the standards, e.g. EMC, and uses a particular clause, where the user manual specifically needs to indicate a requirement for protective measures. https://electronics.stackexchange.com/questions/544125/how-does-a-bare-pcb-product-such-as-a-raspberry-pi-pass-esd-testing-for-ce-mark
EU: Is CE-Marking even needed?
  CE marking is only obligatory for products for which EU specifications exist and require the affixing of CE marking.
  Not applicable for resistors and other components

## Slide 10: Intended Purpose
Often synonymously referred to as “intended use”
Cornerstone for:
  Classification as a medical device
  Classification of the medical device
  What needs to be proven in the clinical evaluation
  Reimbursement (may require particular wording, also in indications for use)
  Liability
Note: The MDR also applies for some devices without a medical intended purpose (e.g. cosmetic lenses, aesthetic implants).

## Slide 11: Intended Purpose
Claims: what the device does
  performance claims
  benefit claims
  non-clinical claims, list for clarity: other technical claims not to be evaluated in the CER, but can be claimed in the labeling and marketing
  Disclaimers
  risks and side-effects
Intended patient population
  demographics (not diseases): age, weight, gender, ethnicity (e.g. AI trained on skin type), nationality, ..

## Slide 12: Intended Purpose
Strategy:
  FDA submissions
    “Me-too strategy”: follow the intended purpose of a previously cleared predicate device, even up to the point of copying its 510(k) submission. This is the easiest, least risky and most effective path to get to the market. (best practice: browse FDA database for predicates in same product category)
    “Me-too +”: while generating revenue with the first, submit a second, high-risk submission with claims for an innovative device
    Classification as a medical device:
      Note that exemptions apply for certain devices (e.g. Non-Device clinical decision support, see CDS)

## Slide 13: Intended Purpose
General vs. narrow intended purpose:
  Europe:
    Innovative devices should ideally/ theoretically claim a narrow scope, then extend it gradually through additional studies when the first device is already on the market.
    Being specific may significantly reduce the required efforts, e.g. for:
      Clinical evaluation: indication, patient population
      Design and validation: patient population
      Usability validation: user groups (number of groups, homogeneous?, trained?)
  FDA
    The “me-too strategy” often leads to a general intended purpose
    The FDA’s guidance document “General/Specific Intended Use - Guidance for Industry” provides indications to “determine whether the addition of a specific indication for use to a medical device cleared for marketing with a general indication for use could trigger the need for a PMA” or a Class III designation [FDA-2020-D-0957].
    Herein, substantial equivalence or non-equivalence is determined in part by general/specific uses. E.g., adding a more specific intended purpose with “treatment character” (e.g. knife for eye surgery or lithotripter) to a general intended use with a “tool” character (scalpel, typically Class I) may lead to a Class III designation.

## Slide 14: Requirements
must
shall
should

## Slide 15: System Design Concepts Full-Stack Web
Full-stack web programming includes:
  front-end: client software (e.g. JavaScript, jQuery, Angular, Vue)
  back-end: server software (e.g. PHP, ASP, Python, Node) including databases (e.g. SQL, SQLite, MongoDB)
Standard design concepts:
  web server:
    Load balancing: distribute traffic to multiple servers, e.g. DNS load balancing (resolve website to multiple IP addresses)
  static assets servers (images/videos)
    content delivery networks: global network of caching servers makes accessing content quick, e.g. pool technique: first user fetches the file, then it remains in cache.
    Distributed file systems (e.g. for users to upload images), e.g. Amazon S3
  database server:
    Use caching services: place popular data in caching layer instead of slow disk (e.g. NYT website).
    Indicing using database schema design: the index points to the data record; use composite indices (an index table, e.g. sorted by longitude, latitude, last active) to make queries fast
    Slave-master replication: only master used to write to, slave databases replicate master for read-only (with a delay). To avoid delay for high priority request, read from master or a cache that is always up-to-date.
    Database sharding: split database into master databases on multiple servers.
      Allows lots of users write to the database simultaneously (e.g. Twitter)
      Verticle: split into databases with different information (users, tweets, comments)
      Horizontal: split same content (e.g. tweets) over multiple machines, method: e.g. userID MOD N => server
    NoSQL databases: not relational (not tables), scale automatically across multiples machines (e.g. MongoDB, Firebase).
  API design (client-server communication): consider transport mechanism (e.g. JSON or protocol buffers), security requirements, support of offline usage
  General remark: Simplicity comes before optimization! No two applications scale the same way. Load and usage scenarios are important.
[TechLead, 2020: Systems Design Interview concepts (for software engineers / full-stack web)]

## Slide 16: Great Programming
Great programming can be practiced.
The core art is problem decomposition (e.g. using layers of abstraction)
Classes should be deep (i.e. simple interface (cost), lots of functionality contained (benefit); shallow classes create unnecessary overhead and complexity).
Ideally write classes for a general purpose (simpler and easier to maintain, special-purpose leads to complexity from sharing information through APIs)
Ideally write APIs for a general purpose
Spend 10% to continue improving your code base (as it will automatically become more complex otherwise); ideally, after a change, it should be designed/structured as if change had been known from the start
[Talk by Ousterhout, John related to: A Philosophy of Software Design]

## Slide 17: Effective Engineering
10x-engineers produce 10x the impact, they do not work 10x the hours.
These engineers, per observation:
  Focus on big levers (work on what has the most impact), e.g. reduce complexity in design, do unit tests where they are most relevant, ..
  Optimize for learning (use opportunities to learn, educate themselves, do side projects, ..)
  Invest in iteration speed (learn and provide tooling, create tools when you need to do something twice, fasten build processes, [learn to focus and complete things in time] ..)
  Validate your ideas aggressively and iteratively, validate the assumptions that go into your ideas (this is sometimes very simple to do)
  Reduce complexity:
    Code and system complexity (easier-to-maintain, easier-to-learn for beginners)
    Product complexity (no clear vision; each feature adds a lot to that)
    Minimize operational burden (at its core, this is a cost of code complexity). With organizational complexity, quality and motivation goes down due to lack of feedback/work in isolation, bus factor goes down.
  Build a great engineering culture
    Candidates like companies with all of the above.
    Resource conflicts: communicate between teams on their priorities. Align priorities, otherwise, understand them to see if possibly your team has to do some of the low-priority work of others
[The Effective Engineer, Edmond Lau]